## Slide 1: MIA Lab Mid-term Presentation: Hypothesis 1: Preprocessing
Project Group 7: Chanae Smith, Tudorita Zaharia, Isabella Torres

## Slide 2
NOISE REDUCTION
High quality images Customized 3T scanner & pulse sequences Denoising could help
NORMALIZATION
Dataset has consistent acquisition parameters and imaging devices across subjects. Sanity check confirmed this
RESAMPLING
Images in native subject space. Resampling would ensure consistent resolution & voxel dims across images
BACKGROUND REMOVAL
The dataset has non-skull stripped T1w and T2w images.
Notes: To develop the hypothesis, we started by exploring the material that was provided to us. We found that preprocessing for medical image analysis typically comes in 4 flavours, so we considered those with respect to our dataset
The first is background removal, where you remove irrelevant areas. In our case, that would be like the skull since the images are non-skull-stripped. So this would definitely feasible for isolating the brain region before further processing.
Next is noise reduction. The HCP uses advanced MRI acquisition techniques that yield high-quality images with reduced noise due to hardware improvements like customized 3T scanners. But, additional denoising techniques could still be beneficial to enhance the clarity of structures, especially for segmentation tasks.
Thirdly, normalization. We took a look at the research paper detailing the acquisition parameters for the images and found that they standardized the data collection protocol by enforcing consistent acquisition parameters and imaging devices across subjects from all sites. So histogram matching or similar intensity normalization methods across the dataset might not be very helpful due to the already existing uniformity. While negative results in research are still results, we would like to focus on something that might be a bit more insightful
Lastly, there are resampling methods. We know that the dataset images are in native subject space. This means that the images are in the original anatomical orientation and resolution as they were acquired from each subject, without being transformed or aligned to a standard template or atlas space. So resampling the images could help with downstream tasks like registration
So based on this, we wanted to develop a hypothesis that would target one or multiple of these 3 types of preprocessing
Resampling is the process of interpolating and adjusting an image to a new grid or voxel size, often to match a different spatial resolution or align with a standard reference space. It involves changing the voxel dimensions, orientation, or resolution to ensure consistency across images or compatibility with a template.

## Slide 3: Hypothesis:
We investigate the combined effects of multiple pre-processing steps on the final evaluation of brain tissue segmentation, and hypothesize that:
Combining denoising and resampling methods leads to additive improvements in segmentation performance over using each method individually.

## Slide 4: Experimental Design
Create datasets with various combinations of pre-processing steps:
  No pre-processing (baseline + skull stripping)
  Denoising only -> Increasing SNR? Gaussian filtering? Edge-aware filtering?
  Resampling only -> Linear interpolation? Spline interpolation?
  Both denoising and resampling
Model Training
  Train the segmentation model on each dataset separately
Performance Comparison
  Evaluate the segmentation results
    DICE
    Hausdorff distance
Evaluation metrics
  Structural Similarity Index Metric
  Mean Squared Error